## Slide 1: RaspberryRemote
A web-based universal remote using LIRC

## Slide 2: Tech Stack
ASP.NET Core
SignalR Core
LIRC

## Slide 3: .NET Core
.NET Core is the open-source successor to the .NET Framework
Introduced in 2016
Implements .NET Standard
Can be compiled and executed on Windows, macOS, or Linux
Can run on top of the .NET Framework or as native code

## Slide 4: SignalR
Simplifies real-time communication between server and clients
Allows messages to be pushed to clients without a request
Utilizes:
  WebSockets (Latest versions of major browsers)
  Server Sent Events (All recent browser versions except IE)
  Forever Frame (IE only)
  AJAX long polling (older browsers)

## Slide 5: LIRC
Linux Infared Remote Control
Package which allows sending and receiving of infared signals
Large database of thousands of pre-configured remotes available at http://lirc.sourceforge.net/remotes/
Also supports training custom devices
Control computer with remote, or remote devices with computer

## Slide 6: Circuit

## Slide 7: Circuit
I used a 220 ohm resistor instead of a 10k ohm resistor – this will depend on your infared LED
These LEDs and receivers worked great for me: https://www.amazon.com/gp/product/B00EFOQEUM/ref=ppx_yo_dt_b_asin_title_o00_s00?ie=UTF8&psc=1
I also added an extra LED in parallel with the infared LED for debugging purposes

## Slide 8: Interaction between .NET Core and LIRC
I use the Process class to interact with the LIRC CLI
  Get a list of valid commands
  Send commands from the webserver to the infared LED
  Listen for infared signals from a configured remote

## Slide 9: Disclaimer
This is a proof-of-concept and the architecture is not designed using industry best practices
Expect bugs 

## Slide 10: Getting valid commands
irsend list “remote_name” “”

## Slide 11: Send commands
irsend send_once “remote_name” “key”

## Slide 12: Listen for signals
irw

## Slide 13: Resources
Proof-of-concept repository here: https://github.com/johnnyRose/RaspberryRemote
Tutorials:
  https://www.hackster.io/austin-stanton/creating-a-raspberry-pi-universal-remote-with-lirc-2fd581
  https://raspberrypi.stackexchange.com/a/70946/98721
Other helpful resources:
  http://www.lirc.org/
  https://raspberrypi.stackexchange.com/a/73070/98721
  https://www.instructables.com/id/Verify-and-Debug-Linux-Infrared-Remote-Control-LIR/
Getting started with .NET Core: https://docs.microsoft.com/en-us/dotnet/core/get-started?tabs=windows
Getting started with SignalR Core: https://docs.microsoft.com/en-us/aspnet/core/tutorials/signalr?view=aspnetcore-2.2&tabs=visual-studio

## Slide 14: Demo?